## Slide 1: BENDIX / KING KAP 140
THE KAP 140 SINGLE AXIS SYSTEM IS AN ENTRY LEVEL DIGITAL PANEL-MOUNT AUTOPILOT, OFFERING LATERAL MODES WITH AN ELECTRIC TRIP OPTION.
THE KAP 140 TWO AXIS SYSTEM PROVIDES BOTH LATERAL AND VERTICAL MODES.
THE KAP 140 TWO AXIS SYSTEM PROVIDES BOTH LATERAL AND VERTICAL MODES WITH ALTITUDE PRE-SELECT.

## Slide 2
1. PITCH AXIS, (P) ANNUNCIATOR
2. AUTOPILOT ENGAGE / DISENGAGE (AP) BUTTON
3. ROLL AXIS (R) ANNUNCIATOR
4. HEADING (HDG) MODE SELECTOR BUTTON
5. NAVIGATION (NAV) MODE SELECTOR BUTTON
6. APPROACH (APR) MODE SELECTOR BUTTON
7. BACK COURSE APPROACH (REV) MODE SELECTOR BUTTON
8. ALTITUDE HOLD (ALT) MODE SELECT BUTTON
9. VERTICAL TRIM (UP/DN) BUTTONS
10. ROTARY KNOBS
11. BARO SET (BARO) BUTTON
12. ALTITUDE ARM (ARM) BUTTON
13. ALTITUDE ALERTER/VERTICAL SPEED / BARO DISPLAY
14. ALTITUDE ALERT (ALERT) ANNUNCIATION
15. PITCH TRIM (PT) ANNUNCIATION
16. PITCH MODE DISPLAY
17. ROLL MODE DISPLAY
18. AUTOPILOT ENGAGED (AP) ANNUNCIATION

## Slide 3: READING THE DISPLAY
INFORMATION ALONG THE TOP LINE OF THE DISPLAY INDICATES THE MODES THAT ARE CURRENTLY ACTIVE. THE INFORMATION ON THE BOTTOM SHOWS WHAT WILL HAPPEN IN THE FUTURE.
IN THIS EXAMPLE THE AUTOPILOT IS IN HDG (TRACKING THE HEADING BUG) AND VS MODES AND THE ALT MODE IS ARMED TO CAPTURE 7,000 FEET.
IF THE ALT MODE IS NOT IN ARM, THE AUTOPILOT WILL NOT CAPTURE THE SELECTED ALTITUDE.

## Slide 4: SCENARIO INDEX
1. TAKEOFF AND CLIMB TO ALTITUDE.
2. GPS / VLOC TRACK CAPTURE.
3. PROCEDURE TURN TO ILS APPROACH.
4. ILS APPROACH.
5. GPS APPROACH.

## Slide 5: TAKEOFF TO ASSIGNED ALTITUDE
STEP # 1.
THE DG / HSI HEADING BUG IS SET TO 080°, THE RUNWAY HEADING FOR TAKE OFF.
THE AIRCRAFT IS AIRBORNE AND ESTABLISHED IN CLIMB.
THE AP AND HDG BUTTONS ARE PRESSED.
VS MODE 500 FPM ACTIVE.

## Slide 6: TAKEOFF TO ASSIGNED ALTITUDE
STEP # 2.
THE DG / HSI HEADING BUG IS SET TO THE NEW HEADING OF 010°
7000’ IS SELECTED USING THE ROTARY KNOBS.
THE ARM BUTTON IS PRESSED TO ACTIVATE ALTITUDE CAPTURE.

## Slide 7: TAKEOFF TO ASSIGNED ALTITUDE
STEP # 3.
THE AIRCRAFT IS RESPONDING TO THE NEW HEADING OF 010°.
CLIMB RATE IS DECREASED TO 200 FPM BY PRESSING DN 3 TIMES (300 FPM).

## Slide 8: TAKEOFF TO ASSIGNED ALTITUDE
STEP # 4.
THE AIRCRAFT HAS REACHED ALTITUDE AND AUTOMATIC ALTITUDE CAPTURE OCCURS.
THE TURN IS COMPLETE AND THE AIRCRAFT IS ESTABLISHED ON A HEADING OF 010°.

## Slide 9: GPS / VLOC TRACK CAPTURE
STEP # 1.
CONTINUING LEVEL ON 010°, A TRACK IS ENTERED INTO THE GPS, OR A VOR / LOCALIZER FREQUENCY IS TUNED.
A 30° INTERCEPT ANGLE IS DESIRED.

## Slide 10: GPS / VLOC TRACK CAPTURE
STEP # 2.
THE HDG BUTTON IS PRESSED TO ACTIVATE ROL MODE, ALLOWING AN “ALL ANGLE INTERCEPT”.
THE GPS / VLOC DESIRED TRACK (DTK) IS SET ON THE OBS.
THE NAV BUTTON IS PRESSED TO ARM TRACK CAPTURE.

## Slide 11: GPS / VLOC TRACK CAPTURE
STEP # 3.
WHEN THE ANTICIPATED INTERCEPT POINT IS REACHED THE ROL MODE SEQUENCES TO NAV MODE AND A RIGHT TURN IS INITIATED BY THE AUTOPILOT.

## Slide 12: GPS / VLOC TRACK CAPTURE
STEP # 4.
THE TURN IS COMPLETE AND THE AUTOPILOT IS TRACKING THE GPS / VLOC TRACK.

## Slide 13: PROCEDURE TURN TO ILS APPROACH
STEP # 1.
THE AIRCRAFT IS HEADING 270°.
THE ILS FRONT COURSE IS SET TO 058° ON THE OBS.
THE REVERSE COURSE REV BUTTON IS PRESSED.

## Slide 14: PROCEDURE TURN TO ILS APPROACH
STEP # 2.
WHEN THE CAPTURE POINT IS REACHED THE REV MODE AUTOMATICALLY ACTIVATES AND THE AUTOPILOT TURNS THE AIRCRAFT TO THE ILS BACK COURSE OF 238°.

## Slide 15: PROCEDURE TURN TO ILS APPROACH
STEP # 3.
AT THE DESIRED POINT THE HEADING BUG IS SET TO 238° AND THE HDG BUTTON IS PRESSED TO ACTIVATE THE PROCEDURE TURN.

## Slide 16: PROCEDURE TURN TO ILS APPROACH
STEP # 4.
AT THE DESIRED POINT THE HEADING BUG IS SET TO 103° AND THE AIRCRAFT TURNS 180° TO INTERCEPT THE ILS FRONT COURSE.
THE APR BUTTON IS PRESSED IN ORDER TO INTERCEPT THE ILS FRONT COURSE OF 058°.

## Slide 17: ILS APPROACH
STEP # 1.
APPROACHING THE LOCALIZER, APPROACH COUPLING OCCURES AND HDG MODE AUTOMATICALLY SEQUENCES TO APR MODE .
THE AIRCRAFT TURNS TO INTERCEPT THE LOCALIZER 058°.
GLIDESLOPE MODE IS AUTOMATICALLY ARMED.

## Slide 18: ILS APPROACH
STEP # 2.
TRACKING THE LOCALIZER ALTITUDE HOLD DISENGAGES WHEN THE AIRCRAFT CAPTURES THE GLIDE SLOPE.
THE ALT ANNUNCIATOR EXTINGUISHES AND GS IS DISPLAYED.
THE AUTOPILOT MAKES BANK AND PITCH CHANGES TO MAINTAIN THE LOCALIZER AND GLIDE SLOPE.

## Slide 19: ILS APPROACH
STEP # 3.
APPROACHING THE DH THE PILOT DEPRESSES THE AP BUTTON TO DISENGAGE THE AUTOPILOT AND HAND FLY THE AIRCRAFT.
THE FLASHING AP FUNCTIONS ARE DISPLAYED AND THE DISCONNECT TONE SOUNDS.

## Slide 20: ILS APPROACH
STEP # 4.
THE PILOT INITIATES THE MISSED APPROACH AND STABILIZES A CLIMB.
THE HEADING BUG IS SET TO THE MISSED APPROACH HEADING OF 090°, ALT IS SET USING THE ROTARY KNOBS.
THE AUTOPILOT IS ACTIVATED, THE HDG BUTTON IS PRESSED AND VS IS SET FOR THE DESIRED CLIMB RATE.

## Slide 21: GPS APPROACH
STEP # 1.
THE AUTOPILOT IS IN HDG MODE APPROACHING THE IAF (INTERMEDIATE APPROACH FIX).
THE OBS IS SET TO THE GPS INBOUND TRACK OF 058°.

## Slide 22: GPS APPROACH
STEP # 2.
REACHING THE IAF, THE HEADING BUG IS SET TO THE OUTBOUND TRACK OF 238°.
THE AUTOPILOT COMMANDS THE TURN.
PILOT ADJUSTS THE HEADING BUG ACCORDINGLY TO MAINTAIN TRACK.

## Slide 23: GPS APPROACH
STEP # 3.
AT THE DESIRED POINT, THE PILOT ADJUSTS THE HEADING BUG TO 283° TO COMMENCE THE PROCEDURE TURN.

## Slide 24: GPS APPROACH
STEP # 4.
ON A HEADING OF 103°, THE PILOT PRESSES APR TO ARM APPROACH MODE.
THE HEADING BUG IS SET TO 058° IN ANTICIPATION OF THE INTERCEPT.

## Slide 25: GPS APPROACH
STEP # 1.
APR MODE CAPTURE OCCURS, THE AUTOPILOT INITIATES A LEFT TURN TO TRACK THE 058° GPS TRACK.

## Slide 26: GPS APPROACH
STEP # 2.
AT THE FAF, ALT IS PRESSED TO ACTIVATE VERTICAL SPEED MODE. THE DESIRED DESCENT RATE IS SELECTED USING THE DN BUTTON (ONE PUSH PER 100 FPM).
AIRSPEED IS CONTROLLED USING THE THROTTLE.

## Slide 27: GPS APPROACH
STEP # 3.
AT THE MDA, THE ALT BUTTON IS PRESSED CAUSING THE AUTOPILOT TO LEVEL OFF AND MAINTAIN ALTITUDE.
AT THE MAP THE PILOT DEPRESSES THE AP BUTTON TO DISENGAGE THE AUTOPILOT AND HAND FLY THE AIRCRAFT.

## Slide 28: GPS APPROACH
STEP # 4.
THE PILOT INITIATES A MISSED APPROACH AND STABILIZES THE CLIMB. THE HEADING BUG IS SET TO THE MISSED APPROACH HEADING OF 090°, AND THE DESIRED ALTITUDE.
THE PILOT PRESSES AP, HDG, AND TOGGLES UP TO SELECT THE APPROPRIATE VS, AND ARM TO CAPTURE THE ALTITUDE.